## Slide 1: 5G Network Slice
Ravi Shankar Prasad – M11202816
Tobias Erik Rosengren – E11302004

## Slide 2: The V2X Challenge & 5G’s Solution
V2X (Vehicle-to-Everything) communication is vital for autonomus driving, traffic efficiency and safety
Demands stringent Quality of Service (QoS):
Ultra-low-latency
High reliability
High throughput for infotainment/maps
5G’s Promise:
5G is designed to support these demands, partially through Network Slicing
Network Slicing allows dedicated, isolated ”virtual networks” (slices) tailored to specific V2X services

## Slide 3: Project Objective: Achieving V2X QoS
Primary Goal: To design, simulate and test a 5G network slicing implementation to demonstrate the possibility of achieving the strict QoS requirements
V2X: Moderate throughput (50-100 Mbps) but strict latency
eMBB: Highest throughput (1 Gbps) but variable latency
mMTC: Low throughput (<10 Mbps), bursty traffic

## Slide 4: Methodology & Tools
Simulation Environment:
  Core Network (5GC): Open5GS – Open-source implementation of 5G Core Network functions
  Radio Access Network (RAN) / User Equipment (UE): UERANSIM – Open-source 5G gNodeB and UE simulator
Tools:
  Wireshark
  iperf3
  MongoDB

## Slide 5: System Framework

## Slide 6: System Architecture

## Slide 7: Target Metrics
Throughput:
V2X: Moderate throughput (50–100 Mbps)
eMBB: Highest throughput (∼1 Gbps)
mMTC: Low throughput (<10 Mbps), bursty traffic.
Latency
V2X: <10 ms (meets safety-critical requirements).
URLLC: 1–5 ms (industrial automation use case).
eMBB: 20–100 ms (tolerable for video streaming)

## Slide 8: Results
Successful Core Network Operation:
  Successfully built and configured Open5GS and UERANSIM components
  5G registration and session establishment
V2X E2E Connections:
  UE to open5GS
  UE to UE
  UE to AWS
  UE to QEMU

## Slide 9
Metric | UE1 – Host Machine (Loopback, Low-Latency Slice) | UE2 – VM (QEMU) (Bridged, High-Throughput Slice)
gNB IP | 127.0.0.1 (loopback) | 192.168.122.234 (VM bridge IP)
gNB → AMF IP | 127.0.0.5 | 192.168.122.1 (host IP)
UPF GTP-U IP | 127.0.0.7 | 127.0.0.7
Assigned UE IP | 10.45.0.2 | 10.45.0.5
Network Slice Type | SST: 1 (Low-latency slice) | SST: 1 (High-throughput slice)
Expected Latency | ≤ 10 ms (local loopback + low-latency slice) | ≤ 20 ms (bridged interface + high-throughput slice)
Achieved Latency | 1.3 ms (ping to 10.45.0.1) | 10% packet loss
Expected Throughput | ~80–100 Mbps | ~100–150 Mbps
Achieved Throughput | 92.4 Mbps (measured via iperf3) | 85 Mbps (no GTP-U traffic received by UPF)
PDU Session Status | Established | Established
uesimtun0 Assigned IP | 10.45.0.2 | 10.45.0.5
Ping to 10.45.0.1 | Success | 10% packet loss

## Slide 10: UE to UE

## Slide 11: UE to AWS

## Slide 12: UE to Open5GS

## Slide 13: Qemu UE

## Slide 14: Demo Outline
Open5gs and UERANSim system
UE to Open5GS connection
UE to UE connection
UE to IoT things
App hosted on AWS
One UE to UE with one UE hosted on QEMU

## Slide 15: Demo

## Slide 16: Discussion
Managed to setup a simple V2X 5G Network with simulated UE
VM Configuration issues and time constraints lead to the Network Slicing implementation not functioning correctly => Unfortunately cannot verify target metrics throughput and latency in Network Slicing
Open5GS: It is possible to replace 5G Core with free5GC instead

## Slide 17: Conclusion and Future Work
Conclusion:
  Sucessfully designed, simulated and validated a simple 5G network framework for V2X communications
  Using Open5GS and UERANSIM, demonstrated feasability of 5G Networks for V2X
Future Work:
  Troubleshoot and correctly implement network slicing
  Explore dynamic slice management for real-time traffic fluctuation
  Integrate with more realistic traffic models

## Slide 18: References
Mendes, B., Araújo, M., Goes, A., Corujo, D., & Oliveira, A. S. (2025). Exploring V2X in 5G Networks: A Comprehensive Survey of Location-Based Services in Hybrid Scenarios. Vehicular Communications, 100878.
Github: https://github.com/ontherays/5G_network_Slice_iiotntust

## Slide 19: Thank you for listening